## Slide 1: Address Space
1kb BAR register
Statistics1-4
  Address:0x000000, 0x000004, 0x000008, 0x00000C
  Read only
  32b
  Statistics1: ingress pipeline duty cycle: #bus cycles used in
    Divide by xxx, multiply by 100 to get pipeline utilization
  Statistics2: egress pipeline duty cycle: #bus cycles used in
    Divide by xxx, multiply by 100 to get pipeline utilization
Free1-4
  Address: 0x000030, 0x000034, 0x000038, 0x00003C
  Read and write
  32b – MSB (but31 is full flag, bits 30:0 are data
  Free1: free value store address for 64Byte value in BRAM
  Free2: free value store address for 4kByte value in SSD
  Free3: TBD
  Free4: TBD
Free1-4M,
  Address: 0x40, 0x44, 0x48, 0x4C
  Same as free1-4 but for “medium sized” memory chunks
Free1-4L
  Address 0x50, 0x54, 0x58, 0x5c
  Same as free1-4 but for “large sized” memory chunks
Del1
  Address: 0x000020
  Read only
  32b – MSB (bit31) is empty flag, bits 30:0 are data
  Del1: freed-up address in value store (to be added to free list again)
Rev
  Address 0x0000f0
  Read only
  32b
  Firmware revision
Free1_reg
free1_full
free1,
free1_wr
Free2_reg
free2_full
free2,
free2_wr
Free3_reg
free3_full
free3,
free3_wr
Free4_reg
free4_full
free4,
free4_wr
stats1
stats2
stats3
stats4
del1_ety
del1
del1_rd
Revision

## Slide 2: Address Space
Flush Request
  32 bit, value 0 or 1
  Address 0x000000e0 read only
Flush Ack
  32 bit, value 0 or 1
  Address 0x000000e4 write only
Flush Done
  32 bit, value 0 or 1
  Address 0x000000e8 read only
Software defined reset:
  32 bit, value 0 or 1
  Address 0x00000010 write only
  Currently nonfunctional
ICAP:
  Address 0xf4
  Push a bitstream to this address to reconfigure the reconfigurable portion
  Currently nonfunctional
Flush_req
Flush_ack
Flush_done
flushreq
flushdone
flushreq